# Self Similarity with CBR Filler Traffic

In this chapter we show how the CBR filler traffic affects the burstiness, variability, and the self-similarity of the aggregated traffic on the center link. In order to better assess this effect we study both the individual flows (i.e. pre-existing traffic and filler traffic) and the aggregated flow.

Recall from chapter two that among the information we collected from each simulation output was the amount of bytes transmitted by each flow over the center link every 0.1 seconds. This aggregation of bytes every 0.1 seconds, forms a time series of 18000 observations (simulation time was 30 minutes) that corresponds to byte transmissions on the center link. We then examine these time series for self-similarity and long-range dependence by using three different statistical methods namely, the absolute value method, the Periodogram method, and the wavelet analysis method. Theses methods are described fully in [1, 3, 36] and a brief introduction can be found in section 1.5.

Each of the following sections relates to the effect of the CBR filler traffic on the self-similarity of both the aggregated traffic and the individual flows as some parameter changes (i.e. link bandwidth, CBR rate, filler buffer size, CB packet size, or link latency).

## Link bandwidth:

Link bandwidth is expected to have a major impact on the self-similarity of the aggregated traffic as well as on the filler traffic itself. This is due to the fact that the link bandwidth controls the capacity of the line and hence the shape and the pattern of the traffic on the line. Figure 5.1 shows the value of the Hurst parameter H as the link bandwidth changes (this is for trace 2). The figure shows that there is a cut off point on the link bandwidth before which the H of the aggregated traffic was always less than 0.5 or equivalently, the traffic is not self-similar. This cut off point occurs at link bandwidth of 8 Mbps. Also for bandwidths above this point, the traffic was always self-similar (i.e. H is grater than 0.5). Figure 5.2 shows the results of the three statistical methods for bandwidths 3 Mbps and 10 Mbps (base case).

Figure 5.1: H of the aggregated traffic as a function of the link bandwidth for trace 2.

(a)						(b)

(c)						(d)

(e)						(f)

Figure 5.2: statistical methods for finding H, left: methods results when link bandwidth was 3 Mbps, right: methods results when the link bandwidth was 10 Mbps. (a) and (b) shows Periodogram method, (c) and (d) shows absolute value method, and finally (e) and f) shows the wavelet method.

Our explanation for this change on the self-similarity of the aggregated traffic is based on the amount of bytes transferred. Recall that CBR injects bits in the network at a constant rate of 6 Mbps and the average throughput of the pre-existing traffic was about 1.34 Mbps giving a total of about 7.34 Mbps of aggregated traffic on the center link. Now, it becomes clear why the cut off point on the link bandwidth occurred at 8 Mbps. For all bandwidths less than 8 Mbps that we experimented with (i.e. 2 Mbps, 4 Mbps, and 6 Mbps), the line was always transferring at full capacity and there is no empty room for any possible variability. In other words, the traffic can be modeled as a long ON period with approximately zero OFF periods. Also the utilization of the line was always 100% because the line was always full and the amount of data that we wanted to transmit was much more than what the available link capacity can handle.

Conversely, when the link bandwidth was greater than 7.34 Mbps (i.e. 8 Mbps, 10 Mbps, and 15 Mbps), the aggregated traffic was always self-similar (i.e. H was greater than 0.5). That is because, for bandwidths higher that 7.34 Mbps there will always be some empty room on the line. Hence there is a chance for variability and these empty rooms can some times be exploited by traffic bursts (i.e. network spikes) when the network traffic peaks demanding more bandwidth than what it normally needs. Again, in this case, the process of sending aggregated traffic can be modeled as alternating ON and OFF periods.

We also plotted the amount of bytes transmitted over different time scales (0.1 seconds, 1 second, 10 seconds and 30 seconds). Figure 5.3 shows the amount of bytes transmitted every 10 seconds when different bandwidths were used. From these time series plots, it is clear that the traffic was very bursty when the bandwidth was grater than 7.34 Mbps (figure 5.3 d, e, and f) and, on the other hand, it can be described as smooth when the small bandwidth was used (figure 5.3 a, b, and c).

(a)					(b)

(c)					(d)

(e)					(f)

Figure 5.3: amount of bytes transmitted over the center link aggregated every 10 seconds. (a) Link bandwidth = 2 Mbps, (b) link bandwidth = 4 Mbps, (c) link bandwidth = 6 Mbps, (d) link bandwidth = 8 Mbps, (e) link bandwidth = 10 Mbps, and (f) link bandwidth = 15 Mbps.

H for the individual flows (pre-existing and filler) was also calculated. The results show that H for the pre-existing flow remains constant while varying the bandwidth of the center link. This is an indication that the filler traffic not only has little effect on the pre-existing traffic in terms of performance metrics, as shown in chapter 3, but it even has little effect on the pre-existing traffic in terms of the variability and the burstiness of the traffic. This is illustrated by figure 5.4. The figure also shows that there is a very minor change between the experiments involving filler traffic and those that does not involve any kind of filler. The wavelet method shows that the change on H between different bandwidths was always within the confidence interval of the other values.

Figure 5.4: H of the pre-existing traffic as a function of the link bandwidth for trace 2.

On the other hand, H of the filler traffic was affected by the available bandwidth. Figure 5.5 shows that H of the filler traffic decrease as the amount of available bandwidth increases. When the bandwidth was small (less than 8 Mbps), H seemed to be constant and the bandwidth has no effect on the burstiness of the filler traffic (filler traffic remains very bursty for these small bandwidths). However, with higher bandwidths (grater than 8 Mbps), H decreases significantly and the filler traffic becomes not self-similar.

Figure 5.5: H of the filler traffic as a function of the link bandwidth for trace 2.

In order to explain the behavior of H of the filler traffic, we did a set of experiments with the pre-existing traffic omitted (only with filler traffic). These experiments showed that H of the filler traffic was always not self-similar for all experimented bandwidths. Given that, the decrease of H for the filler traffic can be explained as follows. When the bandwidth was less than the CBR rate, the filler itself was able to fill the line to its full capacity. However, because the pre-existing traffic has higher priority and hence the filler traffic have the chance to send only when there was no pre-exiting traffic present. Hence there will be long ON periods for the filler traffic followed, from time to time, by short OFF periods (those times when the pre-existing traffic is sending). This results in a huge variability (burstiness) of the traffic. In contrast, as the bandwidth increases there will be more room for the filler traffic to flow smoothly with little intervention from the pre-existing traffic.

## CBR rate:

Because both the CBR rate and the link bandwidth share the common effect of controlling the amount of bytes transferred over the line and the shape of the traffic, CBR rate has similar effect on the self-similarity of the aggregated traffic as the link bandwidth. The Hurst parameter of the aggregated traffic remains almost constant for all CBR rates that are less than 9 Mbps then it increases to 0.979 (according to the wavelet method) and finally decreases to –0.29, as illustrated on figure 5.6.

Like the link bandwidth, we relate the change on H of the aggregated traffic to the amount of the data transmitted on the center link. For all CBR rates that are less than 9 Mbps (8 Mbps, 6 Mbps, 4 Mbps, 2 Mbps, and 1 Mbps) the amount of the aggregated transferred traffic was always strictly less than the capacity of the line. This partially full line results on a big variability on the amount of transmitted data and hence self-similar (i.e. bursty) traffic with H around 0.87 (according to the wavelet method). When the CBR rate was 9 Mbps, the amount of aggregated traffic was about 10.34 Mbps (1.34 Mbps of pre-existing and 9 Mbps of filler) that is more than the capacity of the line. However, because 1) the CBR rate is still less than the link bandwidth, 2) the filler buffer size is finite, and 3) the pre-existing traffic does not come on a constant rate, the traffic will consist of short and unexpected OFF periods (when there are no pre-existing packets to send and the filler buffers are empty) followed by long ON periods. These long ON periods that are followed by short OFF periods contributes to the increase on the value of H when the CBR rate was 9 Mbps. When the CBR rate was the same as the link bandwidth, the line was always full and there was no chance for any variability on the amount of the transmitted data. Thus the traffic was no longer self-similar or equivalently the traffic was not bursty. In conclusion, we have high H values for all rates that are less than the capacity of the link and even higher values if the amount of the aggregated traffic is grater than the link bandwidth. However, the traffic was no longer bursty when the CBR rate was grater than or equals to the link bandwidth.

Figure 5.6: H of the aggregated traffic as a function of the CBR rate.

(a)					(b)

(c)					(d)

(e)					(f)

Figure 5.7: amount of bytes transmitted over the center link aggregated every 10 seconds. (a) CBR rate = 2 Mbps, (b) CBR rate = 4 Mbps, (c) CBR rate = 6 Mbps, (d) CBR rate = 8 Mbps, (e) CBR rate = 9 Mbps, and (f) CBR rate = 15 Mbps.

Figure 5.7 shows the amount of transmitted aggregated bytes every 10 second for different CBR rates (2 Mbps, 4 Mbps, 6 Mbps, 8 Mbps, 9 Mbps and 10 Mbps). These time plots supports our explanation for the change of H while varying the CBR rate. These plots show that there was really minor change on H (time series (a), (b), (c), and (d), looks similar) when the rate was less than the link bandwidth and the total aggregated traffic was also less than the available bandwidth. However, when the rate was 10 Mbps, the traffic was just a long ON period and the line was always full resulting in non-self-similar aggregated traffic.

Figure 5.8 shows that, as the CBR rate changes, H for the pre-existing flow remains unchanged. Chapter 3 proves that the filler traffic was unobtrusive to the pre-existing traffic. This figure and also section 5.1 shows a strong evidence that filler traffic has indeed no effect on the self-similarity (burstiness) of the pre-existing traffic as H remains constant for different bandwidths and CBR rates.

Figure 5.8: H of the pre-existing traffic as a function of the CBR rate.

## Filler buffer size

Hurst parameter increases slightly as filler buffer increase, as figure 5.9 illustrates. The change was hardly visible as H was 0.87 when the buffer size was 4 KB and it was 0.909 when the buffer was 32 KB. Moreover, when the wavelet method was used to find H, all values fall into the confidence interval of others. So it is unclear whether the filler buffer has any effect on H of the aggregated traffic. As relates to the amount of transferred data we also find that the line in all cases was around 73 % utilized. This is a further supporting evidence of the claim we made in the above two sections that H of the aggregated traffic is strongly related to the amount of the traffic on the line. Furthermore, we calculated the correlation coefficient between H and the utilization of the line and turns out to be strongly negatively correlated, as the correlation coefficient was –0.6.

Figure 5.9: H of the aggregated traffic as a function of the filler buffer size

Figure 5.10 shows the time plots of the transmitted bytes aggregated every 10 seconds. Plots demonstrate that the filler buffer size is less likely having any effect on the variability of the transmitted aggregated traffic. The plots for different filler buffer sizes looks similar to each other. However, it seems that the traffic peak slightly more when the filler buffer size increases. These higher peaks in experiments involving larger filler buffers are due to the natural increase on the number of accumulated filler packets on the queues.

(a)						(b)

(c)						(d)

Figure 5.10: amount of bytes transmitted over the center link aggregated every 10 seconds. (a) Filler buffer size = 4 KB, (b) Filler buffer size = 8 KB, (c) Filler buffer size = 16 KB, (d) Filler buffer size = 32 KB.

Again, H of the pre-existing flow remains constant while varying the filler buffer size, as figure 5.11 shows. However, figure 5.12 shows that H of the filler traffic decreases as the buffer size increases. This is because larger filler buffer sizes allow more of the originally non self-similar filler traffic to fill the link.

Figure 5.11: H of the pre-existing traffic as a function of the filler buffer size.

Figure 5.12: H of the filler traffic as a function of the filler buffer size.

## CBR packet size

The packet size of the filler traffic seems to have little to do with the self-similarity of the aggregated traffic, as there is only small change on H as the packet size varied. Figure 5.13 shows that H decreases slightly as the packet size increase. The confidence intervals produced by the wavelet method were also overlapping, indicating little effect of the filler packet size on the self-similarity of the aggregated traffic. This could be related to the fact the CBR filler traffic injects a fixed amount of bytes to the network every second. So the size of the packet does not change the amount of the filler traffic injected to the network but rather changes only the number of packets to preserve the same fixed rate.

Also, the time plots of the amount of aggregated traffic shown in figure 5.14 look identical for different packet sizes, which again suggest no or little effect on the shape of the traffic.

Figure 5.13: H of the aggregated traffic as a function of the filler packet size.

(a)						(b)

(c)

Figure 5.14: traffic on center link aggregated every 10 seconds. (a) filler pkt. size = 576B, (b) filler pkt. size = 1500B, and (c) filler pkt. size = 4500B.

Figure 5.15: H of the filler traffic as a function of the filler packet size.

While the self-similarity of pre-existing traffic remains unchanged when using different CBR packet sizes, there is a little increase on H of the filler traffic as the CBR packet size increases, as shown in figure 5.15. However, because the wavelet methods confidence intervals overlap for different packet sizes, it is unclear whether the filler buffer size has any effect on the self-similarity of the filler traffic.

## Link latency

Link latency also has zero effect on the self-similarity of the aggregated traffic on the center link, as shown in figure 5.16. H remains constant for all latencies across all three methods used to calculate H. Also H of the individual flows (pre-existing and filler) remains unchanged while varying the link latency.

Figure 5.16: H of the aggregated traffic as a function of the link latency.

Latency does not have any effect on the shape of the traffic on the line (or specifically, has no effect on the process of dequeueing packets from the buffer). If, instead, the process of receiving the packets were examined, the link latency could have a big impact on the self-similarity of the traffic because then the link latency affects the amount of aggregated bytes. This is true because the link with higher latency can simply be viewed as just the same but longer link. H of the individual flows also remains constant.

## Discussion and conclusions

We used three statistical methods (Periodogram, absolute value and wavelet) to study the sell-similarity of the time series of sending bytes across the center link for each flow and for the aggregated traffic. Results show that the self-similarity of the pre-existing traffic remains unchanged across all simulations. This extends the unobtrusiveness of the filler traffic (shown in chapter 3) to cover also the burstiness and the variability of the traffic, as the introduction of the filler traffic did not alter the values of H for the pre-existing traffic.

We showed that changing the link bandwidth affects the self-similarity of the aggregated traffic as well as the filler traffic. H of the aggregated traffic was always less than 0.5 when the bandwidth was less than the sum of both the filler and the pre-existing traffics. Conversely, higher bandwidths resulted in bursty (self-similar with H>0.5) aggregated traffic. Although, with small bandwidth the filler traffic remains self-similar with H around 0.9, when higher bandwidths were used H of the filler traffic significantly decrease.

Similarly, changing the CBR rate has the same effect on the self-similarity of the traffic. H of the aggregated traffic remains constant when the amount of the CBR traffic and the pre-existing traffic are less the line capacity. This happens when the CBR rate was small. However, when the rate was equal to or higher the link bandwidth, the aggregated traffic was no longer bursty.

Changing the filler buffer size, the CR packet size, or the link latency resulted in little or zero effect on the self-similarity of the aggregated traffic, as the value of H in remains constant. The filler flow, however, was affected by the change on the filler buffer size and by the change on the CBR packet size. As the size of the filler buffer increases, H of the filler traffic decreases. This is due to the increases on the amount of the originally non self-similar CBR traffic on the line. Also, there was a little increase on the H of the filler traffic when larger CBR packet sizes were used. We, finally, showed that the utilization of the line and the value of H are strongly negatively correlated with a correlation coefficient of –0.6.